## Slide 1
Exxsol D40 Supply Chain Risk
Quality • Traceability • Anti-Adulteration
Risk Committee Briefing | Powder Metallurgy Cleaning September 2026
Confidential

## Slide 2
Executive Summary
Confidential
D40 cleans porous PM parts before plating and coating
Cost pressure raises drum adulteration risk
Fake fluid = fire, HSE and quality failures
Defense: authorized supply + CoA + GC-MS
A cheaper drum can cost more than it saves.

## Slide 3
Agenda
Confidential
01
Why D40 specs matter
02
Boiling range & aromatics
03
Supply risk & adulteration
04
Controls & actions
Focus: protect solvent integrity from plant to production line.

## Slide 4
Business Context
Why D40 is on the Risk Agenda
Confidential
PM pores trap oils — need residue-free clean
D40: fast dry, low odor, metal-safe
Not a commodity — specs are critical
Look-alike solvents raise fraud risk

## Slide 5
Product Profile
Exxsol D40 key specifications
Confidential
Spec | Value | Why it matters
Distillation (IBP–DP) | 163–187 °C | Uniform drying; no heavy-end residue
Flash point | ~48 °C | Flammable — ignition controls required
Aromatics | <0.1% | Low odor, safer, clean surface
OEL | 1,200 mg/m³ | 4× safer than white spirit
KB / viscosity | ~31 / ~1.28 mm²/s | Controlled solvency; pore penetration

## Slide 6
Boiling Range
IBP • Dry Point • Narrow window
Confidential
IBP = first drop; Dry Point = last drop
Narrow ~24 °C range = predictable drying
Wide range leaves heavy ends in PM pores
MC / methanol collapses the profile
Adulteration = residue in pores and unstable drying.

## Slide 7
Low Aromatics
Dearomatized = engineered safety
Confidential
Less odor and toxicity for operators
Safer for seals and elastomers
Clean surface for plating / coating
Adulteration voids the certified profile

## Slide 8
D40 vs D60
Same family — different process window
Confidential
 | Exxsol D40 | Exxsol D60 / D60(S)
Boiling range | 163–187 °C | 180–210 °C
Flash point | ~48 °C | ~68 °C
Dry speed | Faster | Slower
Best for | PM fast clean | Higher flash-point needs
D60(S) is a supplier designation — not a different formula.

## Slide 9
Supply Chain Risk
Price pressure raises fraud incentive
Confidential
Middle East conflict stresses feedstock
ExxonMobil +$0.06/lb (Mar 2026)
China terminal price +5% and rising
Wide price gap invites adulteration
Do not buy on price alone. Verify the chain.

## Slide 10
Adulteration Threat
How unscrupulous traders cut cost
Confidential
Mix cheaper MC and methanol into D40
Reuse genuine drums and fake CoA / labels
Looks clear — visual check is not enough
Illegal — voids SDS and fire-risk assessment

## Slide 11
Impact of Fraud
Confidential
Property | Genuine D40 | Adulterated
Distillation | 163–187 °C | Starts ~40 °C
Flash point | ~48 °C | Much lower (methanol ~12 °C)
Cleaning | Controlled, residue-free | Fails or attacks parts
Downstream | Clean active surface | Plating / coating peel

## Slide 12
Enterprise Risk
Confidential
Safety
Fire & SDS breach
Quality
Plating / coating fail
Operations
Scrap & downtime
Reputation
Customer stop-ship
One adulterated lot can hit safety, quality and customer delivery together.

## Slide 13
Distributor QC
Three lines of defense
Confidential
Buy only ExxonMobil-authorized distributors
Batch CoA before goods receipt
Check IBP, flash point and aromatics
Inspect seals, holograms and drum labels

## Slide 14
Traceability
Chain of custody
Confidential
Track lot: plant → ISO tank → drum → line
Barcode drum to CoA in ERP
Annual distributor audit + right-to-audit
Quarantine suspect lots in < 4 hours

## Slide 15
Detection Controls
Confidential
Control | When | Goal
CoA review | Every batch | Match ExxonMobil spec
On-site screen | Each lot | Density / flash / odor flag
GC-MS test | Quarterly + anomalies | Prove purity / ID adulterants
Price check | Ongoing | Spot “too cheap” offers

## Slide 16
Recommended Actions
Risk Committee approval requested
Confidential
1
Authorized distributors only
2
CoA + quarantine all D40 receipts
3
Fund quarterly GC-MS testing
4
ERP drum-to-line traceability
5
Distributor audit within 90 days

## Slide 17
Governance & KPIs
Confidential
Approve Solvent Integrity Program
100% CoA verified before use
Zero unauthorized suppliers
Quarterly GC-MS minimum
Prevention costs less than one fire, scrap event or stop-ship.

## Slide 18
Appendix
Supply chain • GC-MS quality control
Confidential

## Slide 19
D40 Supply Chain
Plant → ISO tank → authorized distributor
Confidential
Confidential

## Slide 20
Traceability Controls
Seals, holograms, QR and CoA at every handoff
Confidential

## Slide 21
Repackaging — Highest Risk Point
Confidential
Plant fills ISO tanks with sealed, labeled product
Ocean / air move under GPS and manifest control
Distributor repack into drums is the fraud window
Demand: tamper seals, holographic labels, batch CoA
Never accept a drum that cannot be traced back to the ISO-tank lot.

## Slide 22
GC-MS Equipment
Gold-standard identity test for D40
Confidential
GC separates the mix
MS fingerprints each peak
Finds MC, methanol, others
Not visible by eye

## Slide 23
How GC-MS Detects Abnormalities
Confidential
Genuine: even C8–C14 peaks
Fake: extra / irregular peaks
Contaminants = fraud signal
Use as lot fingerprint

## Slide 24
Why GC-MS Matters for QC
Confidential
Proves the drum is Exxsol D40 — not a look-alike
Identifies MC (~40 °C) and methanol (~65 °C) peaks
Protects flash-point, residue-free dry and worker safety
Creates auditable evidence for IATF / PPAP material control
Recommended: GC-MS every critical lot + quarterly random drums.

## Slide 25
Questions?
Risk Committee • Exxsol D40 Integrity
Confidential